## Slide 1
PRODUCTION PLATFORM · TECHNICAL REPORT
Data auto-upload flow: from robot health to database and Slack
01
The health check identifies the instrument and gates the upload path; durable records and a separate notification worker make the result traceable.
SEMANTIC NOTE
Robot get_health() = GET /health pre-check. Platform health refresh separately probes backend, Slack, and Google Drive and caches the status.
01 DEVICE / INPUT
02 UPLOAD WORKER
03 CLOUD + DB
04 NOTIFICATION
GET /health
robot reachability + identity
Collect test data
CSV / ZIP via SFTP or SCP
Start upload record
idempotency + file metadata
Scheduler claims lease
background worker + retry
Validate input
size + SHA-256 integrity
Parse & resolve
FileDescription / product / config
Prepare Google Sheet
create or reuse template
Write CSV to Sheets
persist raw test rows
Read summary
test result / tracker data
Upload raw artifacts
Google Drive + links
Write business record
MongoDB; SQLite in simulation
Resolve DB outcome
saved / incomplete / failed
Finish upload record
upload + database status
Queue Slack notification
success or failure payload
Slack worker
send links + error hints
Notification state
success / retry / failed
FAILURE PATH
Persist failure stage / code → retry when retryable → send a failure message to Slack with diagnostics.
Production Platform · Technical Report
Source basis: upload, robot, persistence, and Slack modules
Notes: Source basis: apps/backend/src/modules/robots/api_client/client.py; apps/backend/src/modules/robots/file_transfer.py; apps/backend/src/api/routers/uploads.py; apps/backend/src/modules/uploads/scheduler.py; apps/backend/src/modules/uploads/upload.py; apps/backend/src/modules/uploads/upload_records.py; apps/backend/src/modules/uploads/handler/upload.py; apps/backend/src/modules/system/health.py.
The robot GET /health call is a device pre-check and identity source. It is not the same function as the platform health cache refresh.
The upload pipeline persists an upload record, claims work with a lease, validates the queued file, runs the Google Sheets / Drive workflow, writes the business record, and queues Slack notification work.